## Slide 1: Joint Trip Departure and Arrival Time Choice Model
13th TRB National Planning Applications Conference
May 8-12, 2011. Reno, Nevada
Rosella Picado
Parsons Brinckerhoff

## Slide 2: Motivation
Get rid of fixed time of day factors
Introduce sensitivity to time of day variations in level of service and road prices,
and also to household attributes
Recognize that trip departure and arrival times are not independent
Notes: One of the key contributions of tour-based models is the joint modeling of tour departure and arrival times. It recognizes that the two decisions are related – scheduling a departure time earlier often implies leaving early as well. In a trip-based model, the two decisions are modeled as completely independent of each other.
With a few notable exceptions, the state of the practice for time of day choice in trip-based models continues to be fixed factors, which ignores the effect that increasing congestion has on the diurnal distribution of travel, as well as precludes the examination of strategies aimed at mitigating peak spreading.
In order to be able to incorporate travel time sensitive and other factors in the diurnal distribution of travel, we developed a model of joint departure and arrival time choice, patterned after the tour scheduling models but applied in a standard 4-step trip-based model.

## Slide 3: Model design
Notes: Option a – replaces the diurnal factors completely

## Slide 4: Model design
Notes: Option b – used also as a “post-processor” to allocate traffic into short time periods

## Slide 5: Approach
Apply tour scheduling concepts to trips
Instead of scheduling individual trips, schedule pairs of trips
perId | tripId | depLoc | depTime | arrLoc | arrTime
1 | 1 | home | 8:15 am | work | 8:50 am
1 | 2 | work | 6:25 pm | home | 7:05 pm
2 | 1 | home | 7:30 am | work | 8:10 am
2 | 2 | work | 5:00 pm | gas | 5:35 pm
2 | 3 | gas | 5:45 | home | 5:55 pm

## Slide 6
Approach
Simple tour:
  Home departure + work departure
perId | tripId | depLoc | depTime | arrLoc | arrTime
1 | 1 | home | 8:15 am | work | 8:50 am
1 | 2 | work | 6:25 pm | home | 7:05 pm
2 | 1 | home | 7:30 am | work | 8:10 am
2 | 2 | work | 5:00 pm | gas | 5:35 pm
2 | 3 | gas | 5:45 | home | 5:55 pm

## Slide 7: Approach
Simple tour:
  Home departure + work departure
  Stop time becomes part of trip duration
perId | tripId | depLoc | depTime | arrLoc | arrTime
1 | 1 | home | 8:15 am | work | 8:50 am
1 | 2 | work | 6:25 pm | home | 7:05 pm
2 | 1 | home | 7:30 am | work | 8:10 am
2 | 2 | work | 5:00 pm | gas | 5:35 pm
2 | 3 | gas | 5:45 | home | 5:55 pm

## Slide 8: Data Prep Assumptions
Use “aggressive” trip linking criteria
  Reduces the number of intermediate stops
  Increases the number of paired departure/arrival time alternatives in the estimation sample
  Increases consistency of mode used on both legs of the trip
Exclude un-paired trips from model estimation
Exclude trips with different outbound and inbound modes
Use transposed AM skims to represent PM travel times (later relaxed)

## Slide 9: Diurnal Pattern - HBW
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
DA From Home | 9.6121e-05 | 0.00026338 | 0.0010761 | 0.016971 | 0.053106 | 0.10808 | 0.20684 | 0.23301 | 0.12702 | 0.051364 | 0.029862 | 0.018451 | 0.02571 | 0.028239 | 0.025953 | 0.019878 | 0.014495 | 0.012768 | 0.0077547 | 0.0040723 | 0.004414 | 0.0057364 | 0.0034642 | 0.001375
DA To Home | 0.0077967 | 0.0050012 | 0.0036139 | 0.0019931 | 0.0020309 | 0.0040642 | 0.0093741 | 0.010463 | 0.010063 | 0.0082991 | 0.011766 | 0.027318 | 0.029916 | 0.04169 | 0.085957 | 0.14803 | 0.19913 | 0.15938 | 0.089114 | 0.040757 | 0.028908 | 0.030186 | 0.024691 | 0.020467
SR From Home | 0 | 0 | 0.0023108 | 0.016705 | 0.093372 | 0.10912 | 0.22636 | 0.22591 | 0.10908 | 0.030404 | 0.0085723 | 0.014307 | 0.0095715 | 0.020156 | 0.036571 | 0.042392 | 0.0074344 | 0 | 0.013745 | 0.0077896 | 0.0032888 | 0.0029952 | 0.019701 | 0.00021135
SR To Home | 0.0081028 | 0.0082101 | 0.0018405 | 0 | 0 | 0.02082 | 0.012104 | 0.0020813 | 0.0032794 | 0.020469 | 0.0052318 | 0.032692 | 0.019703 | 0.050707 | 0.13536 | 0.20007 | 0.17385 | 0.13652 | 0.046646 | 0.015278 | 0.028904 | 0.016013 | 0.020409 | 0.041715

## Slide 10: Diurnal Pattern – HBO From Home
Chart: Trip Departure Time
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
DA From Home | 0.00034503 | 5.1323e-05 | 7.833e-05 | 0.00098809 | 0.006139 | 0.016792 | 0.058905 | 0.14753 | 0.10293 | 0.083427 | 0.065819 | 0.056903 | 0.051007 | 0.051752 | 0.061399 | 0.055519 | 0.048198 | 0.064444 | 0.059981 | 0.038514 | 0.0161 | 0.008675 | 0.0035979 | 0.0009092
SR From Home | 0 | 0 | 0.00010785 | 0.00061466 | 0.0050698 | 0.0094763 | 0.073164 | 0.31031 | 0.10474 | 0.046741 | 0.031724 | 0.036643 | 0.024082 | 0.031302 | 0.030017 | 0.045894 | 0.060364 | 0.063656 | 0.075402 | 0.033665 | 0.011353 | 0.0028551 | 0.0018261 | 0.00099594

## Slide 11: Diurnal Pattern – HBO To Home
Chart: Trip Departure Time
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
DA To Home | 0.0048412 | 0.0039222 | 0.001223 | 0.00071952 | 0.00047115 | 0.001569 | 0.0042476 | 0.03311 | 0.040034 | 0.030607 | 0.04458 | 0.06153 | 0.059142 | 0.06355 | 0.09492 | 0.093029 | 0.086355 | 0.085632 | 0.077772 | 0.063558 | 0.060408 | 0.052355 | 0.02584 | 0.010583
SR To Home | 0.0029604 | 0.00178 | 0.00045979 | 0.00045355 | 0 | 0.00040353 | 0.0010945 | 0.0095489 | 0.014651 | 0.010781 | 0.02056 | 0.030002 | 0.03668 | 0.048753 | 0.17238 | 0.13569 | 0.081423 | 0.090231 | 0.088931 | 0.077754 | 0.091015 | 0.057578 | 0.017728 | 0.0091445

## Slide 12: Time of Day Choices (HBW sample size)
 | Inbound Departure Time |  |  |  |  |  | 
Outbound Departure Time |  | 1- Early | 2- AM | 3- MD | 4- PM | 5- Late | Total
 | 1- Early | 19 | 59 | 975 | 926 | 69 | 2,048
 | 2- AM |  | 108 | 1,999 | 4,745 | 415 | 7,267
 | 3- MD |  |  | 206 | 472 | 414 | 1,092
 | 4- PM |  |  |  | 13 | 65 | 78
 | 5- Late |  |  |  |  | 9 | 9
 | Total | 19 | 167 | 3,180 | 6,156 | 972 | 10,494

## Slide 13: Model Specification
Multinomial logit
Utility terms limited to information available after mode choice:
  Travel time
  Travel distance * shift
  Mode indicator (drive alone / carpool)
  Mode indicator * shift
  Household income indicator
Shift variable: measures disutility of time elapsed relative to a reference time of day

## Slide 14: HBW Estimation
Trip Attribute | Coefficient (t-stat)
Travel time (min) | -0.010 (-5.9)
Travel distance (mi), departure time shift | -0.011 (-15.7)
Shared ride, departure time shift | -0.367 (-3.0)
Low income household, AM departure time | -0.623 (-8.9)

## Slide 15: HBW Estimation
 | Coefficient (t-stat) |  | 
Trip Attribute | Joint Model | Home Departure Time | Work Departure Time
Travel time (min) | -0.010 (-5.9) | -0.014 (-7.9) | -0.001 (-0.8)
Travel distance (mi), departure time shift | -0.011 (-15.7) | -0.035 (-14.1) | -0.0002 (-1.1)
Shared ride, departure time shift | -0.367 (-3.0) |  | 
Low income household, AM departure time | -0.623 (-8.9) |  | 

## Slide 16: HBW Estimation
Choice Constants |  | Value (t-stat)
 | Early | -5.73 (-9.1)
 | AM | -1.97 (-3.8)
Departure Time | MD | -1.56 (-3.6)
 | PM | -1.19 (-3.2)
 | Late | 0.0
 | Early | 0.0
 | AM | -1.51 (-5.4)
Arrival Time | MD | -1.28 (-3.5)
 | PM | -2.99 (-6.3)
 | Late | -5.66 (-9.7)
 | Very Short | -6.95 (-16.2)
 | Short | -4.26 (-14.5)
Duration | Medium | -1.69 (-10.8)
 | Long | 0.0
 | Long, AM | -1.49 (-15.7)

## Slide 17: HBO Estimation
Trip Attribute | Coefficient (t-stat)
Travel time (min) | -0.007 (-3.9)
Travel distance (mi), departure time shift | 
Shared ride, start or end in peak | 0.597 (11.3)
Shared ride, start & end in peak | 0.144 (2.8)
Low income household, Early departure time | -0.295 (-2.7)
Low income household, AM departure time | -0.206 (-5.4)

## Slide 18
Model Application
Early
AM
6:00-8:59
TOD combinations by outbound (→) & inbound (←) directions
Trip
Early
Early
AM
Early
Midday
Early
PM
Early
Late
AM
AM
AM
Midday
AM
PM
AM
Late
Midday
Midday
Midday
PM
Midday
Late
PM
PM
PM
Late
Late
Late
PM
15:00-18:59
Midday
9:00-14:59
Late
19:00-20:59
Early
21:00-5:59
Notes: Peak + off-peak trips from mode choice added up and then transposed to OD format to apply the TOD model.

## Slide 19: Model Calibration & Validation
Calibration – reproduce household survey diurnal patterns
Validation – reproduce freeway traffic count patterns
Freeway | Stations | Share of Daily Traffic Volume |  |  | 
 |  | PeMS |  | Model | 
 |  | AM | PM | AM | PM
All | 847 | 17% | 23% | 17% | 23%
I-5 | 140 | 17% | 23% | 16% | 21%
I-10 | 174 | 16% | 23% | 17% | 22%
I-105 | 4 | 18% | 23% | 17% | 22%
I-110 | 73 | 18% | 23% | 17% | 22%
I-210 | 94 | 18% | 25% | 20% | 25%
I-405 | 182 | 17% | 23% | 18% | 23%
I-605 | 109 | 18% | 23% | 18% | 23%
I-710 | 39 | 18% | 24% | 17% | 22%

## Slide 20: Thank you, Peter!