## Slide 1: Effects of Traffic Operation and Technology on Transit Bus Emissions
Ahsan Alam, PhD Student
Dr. Marianne Hatzopoulou, Assistant Professor
Dept. of Civil Engg. And Applied Mechanics
McGill University, Montreal, Canada

## Slide 2: Background
Transportation benefits us by moving people and goods.
More demand, more traffic on road.
Result:
Traffic congestion
Road collisions
Environmental pollution

## Slide 3: Background
Environmental effect
Global warming: greenhouse gas emissions
Transportation is responsible:
23% of total GHG emissions (worldwide)
26% of total GHG emissions (Canada)
74% of transportation emissions: roadway
Health effect
Respiratory, cardiovascular diseases
Premature mortality

## Slide 4: Motivation
Public Transit:
Considered environmentally friendly
But transit can be as polluting as car (per passenger basis) based on
Age
Fuel
Maintenance
Speed
Passenger volume

## Slide 5: Research Question
How to reduce transit emissions?

## Slide 6
How to reduce transit emissions:
By using alternative fuels?
or
By improving traffic operation?
Research Question

## Slide 7: Outline
Simulate transit emissions along the busy corridor in Montreal, Canada (PTV VISSIM)
Compare the emissions of transit buses (using MOVES)
For 2 alternative fuels:
  Ultra low sulfur diesel (15 ppm sulfur content)
  Compressed natural gas (CNG)
Under different traffic operation:
  Transit signal priority (TSP)
  Relocation of bus stops
  Queue jumper lane

## Slide 8: Study Area
165 Bus Route
downtown

## Slide 9: Base Case Emission Modelling
    One bus is tracked over an entire route (NB and SB) through links and bus stops
    Link based emissions:
    NB: 30 links & SB: 34 links
    Sec-by-sec speed profile for each link
    Age distribution:
    58.39% are of 2010 model & 41.61% are of 2009 model
    Fuel:
    Ultra Low Sulfur Diesel (ULSD)
    Compressed Natural Gas (CNG)
    Meteorology:
    Temperature & Humidity

## Slide 10: Base Case Traffic Simulation

## Slide 11: Simulated Bus Speed Profile
Variables | SB | NB
Length (mile) | 4.74 | 4.09
Number of bus stops | 34 | 30
Length of longest link (mile) | 0.3 | 0.3
Length of shortest link (km) | 0.0775 | 0.05
Total travel time (min) | 50.03 | 30.10
Average journey speed (mph) | 5.68 | 8.15
Maximum speed | 28.83 | 27.43
Time spent (sec) during journey | 2,579 | 1,228
Between 0- 1 mph | 1,296 | 279
Between 2-5 mph | 301 | 147
Between 6-15 mph | 517 | 336
Between 15-25 mph | 369 | 437
>25 mph | 96 | 29

## Slide 12: Base Case Emissions
Running Emissions (g/mile)
Dwell Emissions at Bus Stops (g)
 | SB |  |  | NB |  | 
 | Diesel | CNG | Reduction (%) | Diesel | CNG | Reduction (%)
CO2-eq. | 3504.17 | 3092.31 | 11.75 | 2835.85 | 2608.23 | 8.03
PM2.5 | 0.04631 | 0.00704 | 84.79 | 0.03562 | 0.00403 | 88.68
 | SB |  |  | NB |  | 
 | Diesel | CNG | Reduction (%) | Diesel | CNG | Reduction (%)
CO2-eq | 1719.47 | 1358.38 | 21.00 | 668.93 | 528.45 | 21.00
PM2.5 | 0.03544 | 0.00486 | 86.28 | 0.01379 | 0.00189 | 86.28

## Slide 13: Base Case Emissions (SB)
downtown

## Slide 14: Base Case Emissions (NB)
Changes in CO2eq. EFs
Avg. Speed of the NB Bus

## Slide 15: Scenario Analysis
Traffic operation based scenario:
  Transit signal priority (TSP)
  Bus-stop relocation
  TSP+ Bus-stop relocation
  Queue jumper lane
  TSP+Bus-stop relocation+Queue jumper lane

## Slide 16: Scenario Analysis
Traffic operation based scenario:
  Transit signal priority (TSP)
  Bus-stop relocation
  TSP+ Bus-stop relocation
  Queue jumper lane
  TSP+Bus-stop relocation+Queue jumper lane

## Slide 17: Scenario Analysis
Traffic operation based scenario:
  Transit signal priority (TSP)
  Bus-stop relocation
  TSP+ Bus-stop relocation
  Queue jumper lane
  TSP+Bus-stop relocation+Queue jumper lane

## Slide 18: Scenario Analysis
Traffic operation based scenario:
  Transit signal priority (TSP)
  Bus-stop relocation
  TSP+ Bus-stop relocation
  Queue jumper lane
  TSP+Bus-stop relocation+Queue jumper lane

## Slide 19: Scenario Analysis
Traffic operation based scenario:
  Transit signal priority (TSP)
  Bus-stop relocation
  TSP+ Bus-stop relocation
  Queue jumper lane
  TSP+Bus-stop relocation+Queue jumper lane

## Slide 20: Scenario Analysis
Scenario Description | CO2eq (g/mile) for Diesel |  | CO2eq (g/mile) for CNG | 
 | SB | NB | SB | NB
Base | 3504.17 (0%) | 2835.85 (0%) | 3092.31 (11.75%) | 2608.23 (8.03%)
Introduction of TSP | 3031.62 (13.49%)* | 2668.13 (5.91%) | 2709.99 (22.66%) | 2438.94 (14.00%)
Relocating bus-stops to mid-block | 3191.55 (8.92%) | 2849.25 (-0.47%) | 2869.31 (18.12%) | 2639.98 (6.94%)
Introducing TSP and mid-block bus-stop relocation | 3062.49 (12.60%) | 2776.40 (2.09%) | 2770.66 (20.93%) | 2548.81 (10.12%)
Introducing queue jumper lane | 2987.94 (14.73%) | 2802.61 (1.17%) | 2692.23 (23.17%) | 2542.80 (10.33%)
Introducing TSP, queue jumper lane and relocating bus-stops to mid-block | 2887.56 (17.61%) | 2732.60 (3.64%) | 2654.13 (24.26%) | 2504.10 (11.70%)
* Percent reduction in emissions compared to base case

## Slide 21: Results Found
Switching from diesel to CNG fuel could reduce CO2-eq. emissions by 8 to 12 percent.
As the levels of congestion rise, the reduction benefits become higher indicating that the benefit of switching to CNG becomes more apparent under congested conditions.

## Slide 22: Results Found
TSP alone has the ability to reduce emissions significantly for both directions, congested and uncongested.
When TSP is combined with other measures reduction is significant only in the congested direction.
CNG in combination with operational changes further improves emission reductions.
However, many operational changes can achieve better reductions than switching to CNG and maintaining base-case operations.

## Slide 23: Future Research Plan
The effects of varying congestion levels on the performance of traffic operation and technology.
To understand the effects of grade and passenger load factor on transit emissions.

## Slide 24: Present Research
Average speed: 6mph
Grade -7.5%
Grade -5.0%
Grade -2.5%
Grade 0%
Grade 2.5%
Grade 5.0%
Grade 7.5%
Passenger Load Factor (PLF) 0
Passenger Load Factor (PLF) 0.5
Passenger Load Factor (PLF) 1.0
Passenger Load Factor (PLF) 1.5
Passenger Load Factor (PLF) 2.0
Drive cycle
Average speed: 9mph
Average speed: 16mph

## Slide 25: Present Research

## Slide 26: Present Research
Chart: 
| -7.5 | -5 | -2.5 | 0 | 2.5 | 5 | 7.5
series1 | 4677.1613 | 4651.2581 | 5105.4086 | 8118.1828 | 12179.7849 | 16234.4086 | 20432.2581
series2 | 194.8575 | 293.6694 | 1332.6828 | 1113.7608 | 862.5269 | 555.8333 | 734.7581
series3 | 49.0134 | 44.6909 | 98.828 | 163.879 | 309.8387 | 329.4355 | 994.5968
series4 | 73.8683 | 118.3038 | 190.9651 | 163.6048 | 195.1613 | 89.0323 | 75.0806
Chart: 
| -7.5 | -5 | -2.5 | 0 | 2.5 | 5 | 7.5
series1 | 8912.4086 | 9538.4409 | 10936.4516 | 13968.7097 | 17474.6237 | 20821.6129 | 24698.7097
series2 | 526.5699 | 210.9005 | 206.2366 | 296.5323 | 705.5914 | 987.5 | 1059.9731
series3 | 627.2043 | 556.207 | 307.6882 | 419.4355 | 160.8602 | 384.2204 | 321.371
series4 | 492.1237 | 693.1102 | 305.0269 | 508.3065 | 358.4409 | 712.1237 | 855.7258
Avg. speed of 16mph
Box plots
Random seeds

## Slide 27: Present Research
Chart: 
| 0 passenger | 19 passengers | 38 passengers | 57 passengers | 76 passengers
series1 | 12246.9892 | 12702.7957 | 13697.3118 | 14222.6882 | 14550.9677
series2 | 607.5806 | 784.4086 | 367.8495 | 302.9301 | 338.7634
series3 | 618.3871 | 412.2043 | 430.8065 | 441.4785 | 404.0323
series4 | 1058.5484 | 881.2366 | 571.6129 | 449.3817 | 707.2581
At zero slope

## Slide 28: Present Research
At zero slope
At +7.5% slope

## Slide 29: Present Research
At 7.5% slope

## Slide 30: Present Research
Chart: 
| 0 | 0.1 | 0.2 | 0.30000000000000004 | 0.4 | 0.5 | 0.6 | 0.7 | 0.79999999999999993 | 0.89999999999999991 | 0.99999999999999989 | 1.0999999999999999 | 1.2 | 1.3 | 1.4000000000000001 | 1.5000000000000002 | 1.6000000000000003 | 1.7000000000000004 | 1.8000000000000005 | 1.9000000000000006 | 2
Diesel EF(g/VMT) | 974.5172 | 994.3935 | 1003.1097 | 1018.2204 | 1031.1161 | 1046.1226 | 1053.8645 | 1068.6409 | 1076.9247 | 1082.9892 | 1085.6774 | 1099.4301 | 1105.6774 | 1120.2688 | 1133.9677 | 1143.2258 | 1145.2581 | 1147.6237 | 1159.3978 | 1161.7634 | 1166.6989
Diesel EF(g/VMT/pass.) | 242.535 | 122.3304 | 82.7821 | 62.8729 | 51.0304 | 42.84 | 37.2349 | 32.8331 | 29.3493 | 26.4799 | 24.3776 | 22.4731 | 21.0182 | 19.7555 | 18.589 | 17.4582 | 16.4652 | 15.71 | 14.9135 | 14.228
Diesel EF(g/VMT/40 pass.) | 18.589 | 18.589 | 18.589 | 18.589 | 18.589 | 18.589 | 18.589 | 18.589 | 18.589 | 18.589 | 18.589 | 18.589 | 18.589 | 18.589 | 18.589 | 18.589 | 18.589 | 18.589 | 18.589 | 18.589 | 18.589

## Slide 31
THANK
YOU!
http://traq-research.mcgill.ca/Students/Students.html
ahsan.alam2@mail.mcgill.ca

## Slide 32: Traffic Simulation