## Slide 1: Breaking the Static Barrier: Building Regional Support for Implementation of Dynamic Traffic Assignment in Long-Range Planning Processes
TRB Planning Applications Conference
May 5th, 2013
Peter Bosa, Senior Researcher and Modeler
Metro (Portland, OR)

## Slide 2: Breaking the Static Barrier
Portland Metro has spent 3+ years developing regional DTA tools
  Detailed networks, adjusted trip tables
  Conversion of networks to DTA
  Sample outputs
How to convince regional partners to adopt/use new tools? Demonstrating value in additional costs?
  DTA training and workshops
  Collaborative projects
DTA applications in Portland, OR
  Clackamas County Transportation System Plan
  Southwest Corridor Plan

## Slide 3: DTA in Portland, OR Networks
2010 Network
Built from NAVTEQ base, 6” aerial photos, Google Earth and Streetview
  zones : 2,162
  nodes : 12,600
    signalized : 2,200
    stop signs : 2,200
  links : 32,100
2035 Network
Built up from 2010 using regional transportation plan project list
  zones : 2,162
  nodes : 12,800
    signalized : 2,350
    stop signs : 2,450
  links : 33,000

## Slide 4: DTA in Portland, OR Future year peak spreading
Excess Demand
‘Spread’
Demand
‘Spread’
Demand

## Slide 5: DTA in Portland, OR Future year peak spreading
5
Corridor at or above capacity
peak spreading occurs
Corridor with excess capacity
no peak spreading necessary

## Slide 6: DTA in Portland, OR Conversion to DTA
Base networks stored in VISUM, adjusted trip tables loaded from regional TDM
Static assign in VISUM to produce project subarea, optimize signals
Conversion to Dynameq and/or DynusT

## Slide 7: Development of Tools and Outputs Space-time diagrams

## Slide 8: Development of Tools and Outputs Travel time and reliability plots

## Slide 9: Building Regional Support DTA seminars
Regular meetings with regional partners
  Representatives of state, county, city DOTs within Metro jurisdiction
  Interested local consultants
  Limited outside-of-region people
First round of meetings meant to introduce
  Concepts explained to key stakeholders
  Metro-hosted open house to discuss research
  Developers invited to speak
  Held in parallel with training opportunities
Second round of meetings meant to update
  Status of Metro DTA tool development
  Consultants asked to present on local DTA efforts
  Lessons learned to date
  Proof of concept examples
Third round of meetings meant to demonstrate
  Presentation of results from DTA application
  Ask collaborating partners to present

## Slide 10: Building Regional Support Collaborative teams
Local Jurisdiction
Identified project, Local knowledge and experience
Consultant
Independent party, Provides technical oversight
DTA tools and experience, TDM compatibility

## Slide 11: DTA Applications in Portland, OR Clackamas County Transportation System Plan
Local Jurisdiction
Clackamas County
Consultants
Kittelson & Assoc (KAI)
University of Utah

## Slide 12: DTA Applications in Portland, OR Clackamas County Transportation System Plan
Analyze cost-benefit of building arterial extension using transportation funds in Urban Renewal Area
  Six alternatives studied for year 2035
  Full build, capacity improvements, mix of both
Alternatives evaluated on impact to local intersections, outflow capacity of local streets
Lessons-learned:
  Importance of signal timing to DTA
  Signal optimization for future years
  DTA packages vary in effort needed for calibration effort vs. level of detail provided by tool

## Slide 14: DTA Applications in Portland, OR Southwest Corridor Project
Local Jurisdiction
Oregon DOT
City of Portland
Metro
Consultant
DKS Associates

## Slide 15: DTA Applications in Portland, OR Clackamas County Transportation System Plan
Broad level analysis of capacity restriction on arterial related to potential high capacity transit line (LRT or BRT)
  Two alternatives studied: Baseline vs. Build
Decision makers looking at potential auto diversion impacts
  Local streets vs. freeway
  ‘Unserved demand’ related to capacity constraints in super-saturated corridor
Lessons-learned:
  Nuances of traffic flow theory for developing accurate models for subarea
  Ramp meters become EXTREMELY important in future years

## Slide 16
Data
Animation intended for illustration purposes only
Produced by DKS Associates on behalf of SW Corridor project
Data provided by Metro

## Slide 17: Summary and Next Steps
Development of new tools does not necessarily imply early adoption
Important to educate, update, and demonstrate to clients / potential partner agencies
Collaborative efforts with public / private partners builds comfort with tools while providing a framework for increased knowledge building
Develop additional outputs for showcasing benefits of DTA
Implement DTA in Regional Transportation Plan studies
More robust integration of DTA into travel demand modeling process, including DTA transit and model feedback

## Slide 18: Acknowledgements and Questions?
Transportation Research and Modeling Services – Metro
600 NE Grand Ave.
Portland, OR 97232
(503) 797-1700
Peter Bosa
Peter.Bosa@oregonmetro.gov
Partner agencies
  Clackamas County
  Oregon Department of Transportation
  City of Portland
Partner consultants
  Kittelson Associates Inc (KAI) / University of Utah
  DKS Associates