## Slide 1: HELPViz: An Integrated Two-Tiered System for Land Use Modeling, Planning and Visualization for a Mid-Sized Midwestern City
Vince Bernardin, Jr, PhD, RSG
John Gliebe, PhD, RSG
Seyed Shokouhzadeh, Evansville MPO
Vishu Lingala, Evansville MPO

## Slide 2: Background: Regional Plan for Sustainable Development
Evansville recipient of one of HUD’s grants to produce a Regional Plan for Sustainable Development
Part of Evansville’s grant application included the development of regional land use modeling tools
Three-county area - 2010 population of 285,600

## Slide 3: Evansville: History and Future
Moderate, steady growth overall
For most of the past 40 years, building has outpaced actual growth, resulting in increasing vacant housing and businesses
Between 1950 and 2000 lot sizes doubled from 0.29 to 0.63 acres
SEAC hopes to slow land consumption by encouraging denser and infill development
HELPViz model hopefully adds
  Motivation: Look at 2040!
  Realism: what difference can zoning vs. codes make?
Chart: 3-County Historic Residential Vacancy Rate
| 1940 | 1950 | 1960 | 1970 | 1980 | 1990 | 2000 | 2010 | 2020 | 2030 | 2040
Total | 0.040913 | 0.046858 | 0.032269 | 0.052374 | 0.077129 | 0.069367 | 0.092981
Chart: Residential Growth
| 1950 | 1960 | 1970 | 1980 | 1990 | 2000 | 2010
Households | 62918 | 70544.8879 | 76855.2512 | 92657 | 99204 | 108241 | 115664
Residential Acres | 18012.5555 | 25068.0371 | 31269.2365 | 42525.9309 | 53585.008 | 67892.8576 | 79997.3146

## Slide 4: Land Use Tools vs. Models
Existing options didn’t seem to offer all Evansville wanted
Land Use Planning Tools
  I-PLACE3S
  EnvisionTomorrow
  CommunityViz
  Etc.
Great for visualization
Good for public / planners developing scenarios by fiat
Little/no forecasting ability
No realistic policy sensitivity
Land Use Forecasting Models
  DRAM/EMPAL
  PECAS
  Urbansim
  Etc.
Rigorous forecasts, grounded in econometrics / regional science
  Too much theory?
  Estimation problems?
Calibration is challenging, expensive
vs.

## Slide 5: Solution: Best of Both Worlds
Evansville chose to use an existing land use planning tool and develop a new forecasting tool designed to work together as a single system
CommunityViz
  Manual Scenario Development
    Preferred scenario
  Capacities for HELPViz
  Impact Calculations
  Visualization
HELPViz
  Housing, Employment & Land-use Planning & Visualization Support Model
  Future baseline / status quo scenario
  Policy evaluation scenarios
    (What if we…?)
  Fill in the blanks in manual scenarios
CommunityViz
HELPViz

## Slide 6: CommunityViz’s Role
CommunityViz’s powerful and easy-to-use Build-Out Wizard is a critical input to the HELPViz forecasting model
  Sensitivity to codes:
    Setbacks
    Parking requirements
    Etc.
It’s visualization and impact calculators are powerful tools for communicating results

## Slide 7: HELPViz’s Role
Policy Sensitive Forecasts
  Zoning
  Codes
  Infrastructure
    Transportation
    Water
Easily Estimable
  Avoid endogeneity
Reasonable Runtimes
TransCAD GISDK application
Inputs:
  Regional control totals
  Parcel build-out capacities
  Model networks
  GIS data – slopes, sewerage, etc.
Outputs:
  Future TAZ for travel model
  Future Parcels for CommunityViz

## Slide 8: HELPViz Scale – Both Zones AND Parcels
Existing models use either zones or parcels
HELPViz uses BOTH zones and parcels
Method: Spatial Nested Logit Models
  Information about parcels attractiveness influences allocation to zones
  Growth allocated first to zones, then parcels within each zone
Some behavioral plausibility
  choice of neighborhood and particular property?
Really, econometric framework for:
  estimating sensitivities of growth to various factors
  accounting for some spatial autocorrelation
  handling information, observations at different scales
Information
Allocation

## Slide 9: HELPViz – Residential Models
Vacancy Model
  Takes user HU vacancy rate
  Adjusts control total
  Allocates any new vacancies
  Adjusts residential capacities
Intermediate level nests
  Single Family
  Multi-Family
Vacancy Allocation
Control Total
Single Family
Multi-Family
Parcel
Zone

## Slide 10: HELPViz – Commercial & Industrial Models
Intermediate level nests
  Existing Establishment
  New Development
Units conversion
  Upper levels (TAZ & intermediate) allocate employees
  Lower level allocates sq. ft. of new space to parcels
  Unit conversion
Control Total
New Development
Existing Establishment
Parcel
Zone

## Slide 11: HELPViz – Theory Scorecard
Growth Allocation Model
  Exogenous control totals for regional growth
  Only allocates new growth
Misc. Theory
  No assumption of equilibrium (or of not)
  Path dependence through accessibility to recent growth
  No attempt to simulate individual agents/choices
Statistical Method
  Logit framework for econometric basis of sensitivities
  Allows as many variables as data will support
Sensitivity to Transportation Infrastructure
  Sensitive to network
  Not sensitive to congestion
Decade time steps

## Slide 12: HELPViz – Simultaneous Estimation
Observations at both zonal and parcel level (2000-2010)
  Zones: Census, vetted employment
  Parcels: Assessor’s data & building permits
  Possibly first application to estimate NL with nest observations
Simultaneous, maximum composite log likelihood
  LLTOT = LLTAZ + LLPARCEL
  Must weight/convert parcels observations (sq. ft.) to be consistent with zonal observations (employees)
  Simultaneity & use of application code -> no calibration
Genetic Algorithm
  Population of solutions / starting parameters
  Evaluate each member’s fitness (LL)
  Fit solutions survive, mate & mutate; otherwise die off
  Computationally intense, but eventually finds solution
  Allows inequality constraints (upper and lower bounds)

## Slide 13: HELPViz – Estimation Results
Goodness-of-fit: rho-squared (vs. 0)
Residential Growth 2000-2010
Observed Modeled
 | TAZ | Parcel | Overall
Residential | 0.441 | 0.409 | 0.423
Commercial | 0.243 | 0.237 | 0.241
Industrial | 0.030 | 0.348 | 0.066

## Slide 14: HELPViz – Factors Affecting Growth
Residential Growth
  Near new homes last decade
  Accessible, but not too accessible
  Further from jobs
  But close to retail
  Walking distance to shopping (MF)
  Bias against KY
  Not sloped
  Not floodplain
  Existing sewer
  Zoned Agriculture
  Zoned Residential
Commercial Growth
  Existing Commercial
  Bias against KY
  Near new homes last decade
  Close to arterial intersections
  Arterial frontage
  Zoned Commercial
  Zoned Agriculture
  Not sloped
  Not floodplain
  Existing sewer
  Larger parcels
Industrial Growth
  Existing Industrial nearby
  Access to truck portals
  Zoned Industrial
  (or Agriculture)
  Not sloped
  Existing Sewers
  Rail access

## Slide 15: HELPViz – History & Future? (1940-2040)

## Slide 16: HELPViz – History & Future? (1940-2040)

## Slide 17: HELPViz – History & Future? (1940-2040)

## Slide 18: HELPViz – History & Future? (1940-2040)

## Slide 19: HELPViz – History & Future? (1940-2040)

## Slide 20: HELPViz – History & Future? (1940-2040)

## Slide 21: HELPViz – History & Future? (1940-2040)

## Slide 22: HELPViz – History & Future? (1940-2040)

## Slide 23: HELPViz – History & Future? (1940-2040)

## Slide 24: HELPViz – History & Future? (1940-2040)

## Slide 25: HELPViz – History & Future? (1940-2040)

## Slide 26: HELPViz – Envisioning Alternatives
HELPViz will be used to develop alternative scenarios too
Five main ‘knobs’
  Overrides: the user can specify what does (or doesn’t) happen in particular locations and let the model figure out the rest
  Vacancy Rate: assuming lower vacancy rates can result in infill (but how to make that happen?)
  Codes / Capacities: capacities can be recalculated based on changes to setbacks, parking requirements, etc.
  Zoning: the model can be used to test the effect of alternative zoning
  Infrastructure: the model can test the effect of providing new roads or sewers

## Slide 27: Evansville: Land-use development Scenarios
Transportation and Housing important components of the RPSD
Transportation and Housing scenarios
Four housing development scenarios
Measure transportation demand
Measure fiscal and environmental impacts
Notes: The Evansville MPO wanted to perform scenario planning as part of the RPSD
Transportation and housing are the major components of the plan along with environment and economic development.
The table in the slide shows 4 housing scenarios being developed
These scenarios will be presented at public meetings with the help of CommunityVIZ
The fiscal, social and environmental impacts of the development will be calculated using the CommunityVIZ common impact wizard
Helps decision makers in making informed decisions about future growth

## Slide 28: Impacts of Land-use development
Pictures show fiscal impacts of 2 development scenarios in Town of Kernersville, NC
Source: http://placeways.com/communityviz/gallery/casestudies/pdf/Kernersville.pdf
Fiscal Impacts
Expansion, future operations and maintenance of infrastructure Transportation: Road network Bike & Ped facilities Transit system Water and Sewage lines
Environmental Impacts
Land consumption Air Quality Water runoff

## Slide 29: HELPViz Scale – Both Zones AND Parcels
Existing models use either zones or parcels
HELPViz uses BOTH zones and parcels
  Information is available at both levels
  Observations are available at both levels
Zones
  Auto-based accessibilities
  Households from Census
  Vetted employment #’s
Parcels
  Many attributes
  Assessor’s data
Need to work with both anyway
Information
Allocation