## Slide 1: 2015 GDOT PowerPoint Title Page
Sub Titles Body Text
Project Prioritization Tool for Operational Planning Study
15th TRB National Transportation Planning Applications Conference
Kyle Mote, GDOT PM
Keli Kemp, AICP, HNTB PM
Chandra Khare, HNTB Task Leader
May 19, 2015

## Slide 2
Agenda
Overview of OPS
  Bottlenecks and projects
OPS Project Prioritization Tool
  Project prioritization framework (goals, themes, and performance measures)
  Tool overview
  Project ranking and sensitivity analysis
Findings and Recommendations

## Slide 3
Overview of OPS
Operational assessment of the interstate and limited-access system in the metro Atlanta region
  Identify bottleneck areas
  Identify and evaluate potential low-cost improvements
  Quick implementation – 6 months to 5 years
  Document a prioritized list of operational projects

## Slide 4
Study Area
All limited access facilities in Metro Atlanta
Emphasis on improving the Interstate mainline
22 Corridors

## Slide 5
Identified Bottleneck Locations
129 bottlenecks

## Slide 6
Projects
74 projects at
60 locations

## Slide 7
Project Prioritization Framework –
Development of OPS Goals

## Slide 8
Planning Themes and Performance Measures

## Slide 9
Theme #1: Transportation Mobility
Vehicle Throughput
  Number of vehicles in AM and PM peak hours
Travel Time Savings
  Average travel time saved per vehicle
Reduction of Vehicle Delay
  Daily total vehicle-hours saved
Facilitation of Transit Options
  Qualitative (Yes, No)
  Evaluation factors - Availability of transit option at the location of improvement
Planning Themes and Performance Measures

## Slide 10
Cost
  Quantitative
  Includes Engineering, ROW, and Construction
Benefit/Cost Ratio
  Quantitative
  Benefits include travel time savings and operating cost savings
Theme #2: Financial Feasibility
Planning Themes and Performance Measures

## Slide 11
Anticipated Reduction of Crashes
  Qualitative (High, Moderate and Low)
  Evaluation factors
    Reduction in congestion
    Reduction in conflict points
    Queuing reduction
Anticipated Reduction of Incident Response Times
  Qualitative (High, Moderate and Low)
  Evaluation factors
    Impacts to emergency vehicle accessibility
    Lack of accident accommodations (i.e. no shoulder)
Theme #3: Safety
Planning Themes and Performance Measures

## Slide 12
Facilitation of Current Major Freight Movement
  Qualitative (High, Moderate and Low)
  Evaluation factors
    Improvements to benefit trucks
    Truck percentage in the area of improvement
Connectivity to Current Major Employment Centers
  Quantitative
  Evaluated based on proximity to the activity centers and their associated employment numbers
Theme #4: System Connectivity and
Economic Growth
Planning Themes and Performance Measures

## Slide 13
System Preservation
  Qualitative (High, Moderate and Low)
  Evaluated based on extent of damage/change to existing operating facilities
Level of Environmental Impacts
  Qualitative (High, Moderate and Low)
  Evaluation of Impacts to Environmentally Sensitive Areas (ESA)
    Wetlands and streams
    Historical properties
    Archeological areas
    Endangered species
Theme #5: System Preservation and
Environmental Sustainability
Planning Themes and Performance Measures

## Slide 14
Project Readiness
  Qualitative (High, Moderate and Low)
  Evaluation factors
    Extent of required studies
    Extent of required design
    Is ROW required?
General Constructability And Schedule
  Qualitative (High, Moderate and Low)
  Evaluation factors
    Complexity of construction
    Duration of construction
    Maintenance of traffic complexity and duration
Theme #6: Project Support and Readiness
Planning Themes and Performance Measures

## Slide 15
Project Prioritization Tool Overview
Spreadsheet-based tool
User friendly and transparent
Provide flexibility to:
  Change the themes and performance measures as per the needs of an agency
  Provide a variety of project types and ability to expand the number of projects
  Re-assign weighting factors on the fly

## Slide 16
Project Ranking and
Sensitivity Analysis
Using ordinal rating scheme, each project was assigned a score for each performance measure
Assigned weights to planning themes and individual performance measures
Project points for each theme
Total project points
Ranking established based on total points
Sensitivity analysis was performed to understand impact of each theme – Priority weighting schemes developed

## Slide 17
Priority Weighting Schemes

## Slide 18
Prioritization Tool
Inputs

## Slide 19
Prioritization Tool
Ranking by Scheme

## Slide 20
Prioritization Tool
Project Ranking for various Scenarios

## Slide 21
Findings
Higher performing projects consistently rose to the top regardless of the weighting scheme
74 projects were recommended due to being low-cost strategies
Tool helped with prioritizing and phasing projects
Several of these projects are being implemented at this time

## Slide 22
Recommendations

## Slide 23
QUESTIONS
Kyle Mote, GDOT PM
GDOT Office of Planning
kmote@dot.ga.gov (404-631-1987)
Keli Kemp, AICP – Consultant PM
HNTB Corporation
kkemp@hntb.com (404-943-5747)
Chandra Khare, Consultant Task Leader
HNTB Corporation
ckhare@hntb.com (404-943-5797)