## Slide 1
Logistics Costs in an Advanced Freight Model for Florida
15th TRB National Transportation Planning Applications Conference
May 17-21, 2015

## Slide 2: Introduction
  Tour-based and logistics supply-chain modeling framework (FHWA)
  Applied to Florida
  Logistics Decisions (mode choice )
  Inventory Costs
  Variable Costs
  Commodity Characteristics

## Slide 3: Florida Statewide Freight Model

## Slide 4: Florida Model Integration

## Slide 5: Florida Statewide Freight Model
Firm Synthesis
Supplier Selection
Goods Demand
Distribution Channel
Shipment Size
Mode and Transfers
Synthesizes a list of businesses in Florida, the rest of the US, plus an international sample
Connects suppliers to buyers based on the commodities produced by the supplier and consumed by the buyer
Distributes commodity flows amongst the paired suppliers and buyers
For each buyer/supplier pair, selects whether shipments are direct or involve intermediate handling (intermodal, distribution center)
For each buyer/supplier pair, converts an annual commodity flow to shipments by size and frequency
Identifies the mode for each leg of the trip from supplier to buyer and the transfer locations

## Slide 6
Paths for shipments with complex distribution channel (that are not direct from shipper to buyer) can be multimodal, e.g.
  Truck – Rail – Truck
  Truck – Air – Truck
  Truck – Water
Mode Choice Model
Shipments are Assigned to the Following Modes:
  Truck (Full truck load, less than truck load)
  Rail (Carload, intermodal)
  Water (international, non-international)
  Air

## Slide 7: Mode Choice Model
Model structure based on the Aggregate-Disaggregate-Aggregate (ADA) framework**
  Disaggregation of commodity flows at their production and consumption ends to firm-to-firm flows, shipping and receiving firms paired then treated as a single behavioral unit
  Modeling of logistics decisions that are made by the shipper-receiver pair based on evaluation of the total transport and logistics costs on available paths; and
  Aggregation of individual shipments to origin and destination zones for network assignment purposes
** implemented in Norway and Sweden by de Jong and Ben-Akiva

## Slide 8: Total Cost
Non-Transport Costs
=
ordering
+
carrying
+
damage
+
Inventory in-Transit
+
Safety Inventory
Order preparation, order transmission, production setup if appropriate
Cost of money, obsolescence, insurance, property taxes, and storage costs
Order lost or damaged
Inventory between shipment origin and delivery location
Lost sales cost, backorder cost (Demand and Lead-time uncertainty)
Very important for high-tech commodities (electronics)
Total Costs = Transport costs + Non-Transport costs

## Slide 9: Total Cost Equation
Inventory in-transit cost
Carrying Cost
Safety Stock Cost
Transport and Handling Cost
Ordering Cost
Damage Cost
Variable or Parameter | Description or Interpretation (of Parameters) | Source
Gmnql | Logistics cost (shipper m and receiver n with shipment size q and logistics chain l) | Calculated in the model
Q | Annual flow in tons | FAF
q | Shipment size in tons | Variable
b0ql | Alternative-specific constant | Parameter to be estimated
b1 | Constant unit per order | Parameter to be estimated
T | Transport and intermediate handling costs | network skims, survey data
b2 | Discount rate | Parameter to be estimated
j | Fraction of shipment that is lost or damaged | Survey data or assumed value
v | Value of goods (per ton) | FAF data
b3 | Discount rate of goods in transit | Parameter to be estimated
t | Average transport time (days) | Lookup table (or skims), survey data
b4 | Storage costs per unit per year | Parameter to be estimated
b5 | Discount rate of goods in storage | Parameter to be estimated
a | Constant, set safety stock a fixed prob. of not running out of stock | Survey data or assumed value
LT | Expected lead time (time between ordering and replenishment) | Lookup table (or skims) , survey data
sQ | Standard deviation in annual flow (variability in demand) | Survey data, assumed value
sLT | Standard deviation of lead time | Lookup table (or skims), survey data

## Slide 10: Equation modification
Inventory in-transit cost
Carrying Cost
Safety Stock Cost
Transport and Handling Cost
Ordering Cost
Damage Cost
Term “j” is redundant (the fraction of shipment that is lost or damaged)
Unit = tons (safety inventory level), should be multiplied by the cost of holding safety inventory.
Only “Transport”, “Inventory in-transit” and “Safety stock” costs are reliant on “cost” and “time” from skims (the model performs the shipment size choice before mode choice).
Inventory in-transit cost
Safety Stock Cost
Transport and Handling Cost
Notes: The term “j” in the “inventory in-transit” component of the equation is redundant and should be removed. This term is the fraction of shipment that is lost or damaged and should not be included in the “in-transit inventory” cost component of the total cost since it is being accounted in the “damage cost” component of the total cost.
The “safety stock” component of the equation has a unit of tons which shows the safety inventory level needed to not run out of inventory and should have a dollar unit to be added to other components of the total cost. Therefore, the term should be multiplied by the cost of holding a unit of safety inventory which is shown in the corrected formula below.
Among the total cost components only “Transport”, “Inventory in-transit” and “Safety stock” costs are reliant on “cost” and “time” from skims since the model performs the shipment size choice before mode choice. So, other components can be simply removed from the equation as they have the same values for different mode-path choices.
Further, the safety stock cost component of the total cost equation can be simplified by assuming variability in demand and lead time one at a time or simultaneously depending on the commodity type. For innovative products lead time variability is closer to zero and for functional products demand variability is closer to zero. For products with both functional and innovative characteristics simultaneous variability can be considered as below:
Only variability in demand: 𝑣×𝑎×√((𝐿𝑇×〖𝜎_𝑄〗^2))
Only variability in lead time: 𝑣×𝑎×√((𝑄^2×〖𝜎_𝐿𝑇〗^2))
Variability in both lead time and demand: 𝑣×𝑎×√((𝐿𝑇×〖𝜎_𝑄〗^2)+(𝑄^2×〖𝜎_𝐿𝑇〗^2))

## Slide 11: Product and Supply Chain Types
Safety Stock Cost
Depends on product type
Depends on supply chain type and service level
Depends on product demand patterns
Functional Products | Innovative Products
Mature product | Early life cycle stage
Low product variety | High product variety
Predictable demand | Unpredictable demand
minimize inventory | Deploy significant buffer stocks
Greater reliance on low cost modes | Greater reliance on fast and reliable modes
MATCH
MISMATCH
MISMATCH
MATCH
Functional Product
Innovative Product
Efficient Supply Chain
Responsive Supply Chain
Categorizing commodities
Different parameters

## Slide 12: Model Run Comparisons
Cost type ($) | Formula | Truck | Rail | Air | Water
B0 | Constant | 2,788.9 | 2,739.9 | 99,999,999 | 99,999,999
Transport | Q*C | 247.7 | 266.3 | 4,406.4 | N/A
Inventory in-transit | B3*(t/(24*60))*v*Q/365 | 0.4 | 0.7 | 0.5 | N/A
Safety Stock | B5*v*a*((LT)*(Qsd)^2)+(Q^2+(LTsd)^2))^0.5) | 1,314.5 | 1,452.7 | 1,378.4 | N/A
Ordering | B1*(Q*2000/q) | 50.0 | 50.0 | 50.0 | 50.0
Damage | B2*j*v*Q | 1.2 | 1.2 | 1.2 | 1.2
Carrying | (B4+(B5*v))*((q/2000)/2)) | 15,581.6 | 15,581.6 | 15,581.6 | 15,581.6
TOTAL COST ($) |  | 19,984 | 20,092 | N/A | N/A
Shipment Characteristics | c ($) | 39.9 | 42.9 | 709.7 | N/A
 | t (min) | 1,602.6 | 3,284.8 | 2,380.2 | N/A
 | Q (tons) | 6.2 | 6.2 | 6.2 | 6.2
 | GCD (mile) | 89.5 | 89.5 | 89.5 | 89.5
 | Value ($) | 2,365.3 | 2,365.3 | 2,365.3 | 2,365.3
 | v ($/ton) | 380.9 | 380.9 | 380.9 | 380.9
 | LT (days) | 11.1 | 12.3 | 11.7 | N/A
Commodity | Wood Products
Segment | Internal - Internal
Origin FAF | 129 (Florida, remainder)
Destination FAF | 123 (Florida, Orlando)

## Slide 13: Model Run Comparisons
Cost type ($) | Formula | Truck | Rail | Air | Water
B0 | Constant | 2,309.6 | 5,122.6 | 846.2 | 99,999,999
Transport | Q*C | 17.8 | 22.2 | 777.9 | N/A
Inventory in-transit | B3*(t/(24*60))*v*Q/365 | 3.3 | 26.1 | 13.6 | N/A
Safety Stock | B5*v*a*((LT)*(Qsd)^2)+(Q^2+(LTsd)^2))^0.5) | 31,485.8 | 39,791.6 | 35,245.5 | N/A
Ordering | B1*(Q*2000/q) | 776.0 | 776.0 | 776.0 | 776.0
Damage | B2*j*v*Q | 30.3 | 30.3 | 30.3 | 30.3
Carrying | (B4+(B5*v))*((q/2000)/2)) | 160.0 | 160.0 | 160.0 | 160.0
TOTAL COST ($) |  | 34,783 | 45,929 | 37,850 | N/A
Shipment Characteristics | c ($) | 45.9 | 57.2 | 2,005.0 | N/A
 | t (min) | 578.3 | 4530.2 | 2,367.2 | N/A
 | Q (tons) | 0.39 | 0.39 | 0.39 | 0.39
 | GCD (mile) | 518.5 | 518.5 | 518.5 | 518.5
 | Value ($) | 12,105.9 | 12,105.9 | 12,105.9 | 12,105.9
 | v ($/ton) | 31,201.5 | 31,201.5 | 31,201.5 | 31,201.5
 | LT (days) | 10.4 | 10.4 | 10.4 | 10.4
Commodity | Electronics
Segment | Internal - External
Origin FAF | 123 (Florida, Orlando)
Destination FAF | 379 (North Carolina, remainder)

## Slide 14: Model Run Comparisons
Cost type ($) | Formula | Truck | Rail | Air | Water
B0 | Constant | 2,194.2 | 903.5 | 1,268.0 | 99,999,999
Transport | Q*C | 1.5 | 2.2 | 74.7 | N/A
Inventory in-transit | B3*(t/(24*60))*v*Q/365 | 0.3 | 3.0 | 1.7 | N/A
Safety Stock | B5*v*a*((LT)*(Qsd)^2)+(Q^2+(LTsd)^2))^0.5) | 3,814.5 | 4,781.8 | 4,318.8 | N/A
Ordering | B1*(Q*2000/q) | 50.0 | 50.0 | 50.0 | 50.0
Damage | B2*j*v*Q | 3.7 | 3.7 | 3.7 | 3.7
Carrying | (B4+(B5*v))*((q/2000)/2)) | 287.3 | 287.3 | 287.3 | 287.3
TOTAL COST ($) |  | 6,352 | 6,031 | 5,877 | N/A
Shipment Characteristics | c ($) | 36.7 | 53.2 | 1,801.9 | N/A
 | t (min) | 470.8 | 4,242.3 | 2,285.6 | N/A
 | Q (tons) | 0.04 | 0.04 | 0.04 | 0.04
 | GCD (mile) | 342.0 | 342.0 | 342.0 | 342.0
 | Value ($) | 1,477.2 | 1,477.2 | 1,477.2 | 1,477.2
 | v ($/ton) | 36,061.1 | 36,061.1 | 36,061.1 | 36,061.1
 | LT (days) | 10.3 | 10.3 | 11.6 | 10.3
Commodity | Pharmaceuticals
Segment | External - Internal
Origin FAF | 139 (Georgia, remainder)
Destination FAF | 129 (Florida, remainder)

## Slide 15: Mode Choice Validation Results
Chart: By Mode Tons (%)
| Air | Rail | Truck | Water
Transearch | 0.00053894 | 0.17462 | 0.70992 | 0.11492
Model | 0.00038396 | 0.16877 | 0.75099 | 0.079855
Chart: By Mode Value (%)
| Air | Rail | Truck | Water
Transearch | 0.066347 | 0.12732 | 0.72765 | 0.078687
Model | 0.011481 | 0.036537 | 0.77949 | 0.17249
Calibration of the mode choice model resulted in a relatively good match to the mode choice shares observed in the Transearch data

## Slide 16
www.rsginc.com
Contacts
Kaveh Shabani
kaveh.shabani@rsginc.com
Colin Smith
colin.smith@rsginc.com
Maren Outwater
maren.outwater@rsginc.com