## Slide 1: Portfolio Optimization Using Multiple Scoring Techniques
A Case Study by the Pikes Peak Area Council of Governments
15th TRB National Transportation Planning Applications Conference
May 17 – 21, 2015 Atlantic City, New Jersey
Corridor Management Session: May 19, 2015 8:30 AM – 10:00 AM
Authors:
Craig T. Casper, Pikes Peak Area Council of Governments
Maureen Paz de Araujo, HDR
Katherine Haire, HDR

## Slide 2
01
Multiple Criteria Decision Making
02
Weighted Score Method (WSM)
03
Technique of Order Preference by Similarity to Ideal Solution (TOPSIS)
04
Logic Scoring of Preference (LSP)
05
Selecting a MCDM Methodology

## Slide 3
01
Multiple Criteria Decision Making
“It has become more and more difficult to see the world around us in a unidimensional way and to use only a single criterion when judging what we see.”
Milan Zeleny, Multiple Criteria Decision Making, 1982

## Slide 4: Project Prioritization and Selection for Funding
Many public investment decisions involve multiple objectives and goals
  Multiple Criteria Decision Making (MCDM) are used to rank and select among investment choices
Basic input requirements to MCDM include:
  Evaluation criteria that support identified goals and performance measures
  Scoring of projects for all evaluation criteria
  Weighting for all identified evaluation criteria
Evaluation Criteria | Weight | Normalized Weight
Preservation & Rehabilitation | 12.3 | 0.1230
Mobility & Congestion Reduction | 11.5 | 0.1150
Cost Effectiveness | 8.9 | 0.0890
System Connectivity | 9.3 | 0.0930
Safety | 11.2 | 0.1120
System Security | 7.0 | 0.0700
Environmental Justice | 5.2 | 0.0520
Adverse Impact Reduction | 5.4 | 0.0540
Economic Vitality & Freight Movement | 7.7 | 0.0770
Infill & Redevelopment | 5.1 | 0.0510
Protect Wildlife Habitat | 3.6 | 0.0360
Protect Streams and Reduce Stormwater Runoff | 6.9 | 0.0690
Greenhouse Gas Emissions | 5.9 | 0.0590

## Slide 5: Multiple Criteria Decision Making Methods
Weighted Score Method (WSM)
  Simplest method, method currently used by the PPACG
Technique of Order Preference by Similarity to Ideal Solution (TOPSIS)
  Provides evaluation criteria flexibility (qualitative, quantitative, benefit and cost measures) can be evaluated together)
Logic Scoring of Preference (LSP)
  Mimics flexibility of human decision making process – can specify degree to which multiple criteria should be met jointly versus independently

## Slide 6: Commonalities in Methods
Determining criteria for the project scoring
Determining weight for each criteria
  Stated Preference Surveys
  Analytical Hierarchy Process
Obtaining the score of project i for each criteria j for all i and j
●
●
●
Ranking projects
Cutting projects based on rank

## Slide 7
02
Weighted Score Method (WSM)

## Slide 8: Weighted Score Method
Simplest methodology
Uses multiple criteria and criteria weighting
Requires consistent scale for criteria scoring: either more is better (benefits) or less is better (costs)
Best used to evaluate stand-alone projects using transportation and non-transportation performance measures
Has limited utility for portfolio optimization - identification of the “best set of projects”

## Slide 9: Weighted Score Ranking Process
Obtain the scores for each project i using criteria j for all i and j
  Use consistent scale for all criteria: More is better or less is better
  Use consistent score range for all criteria: The same score range or normalized scoring
Compute the sum of the weighted scores for each project
Rank projects by order of sum of the weighted scores
Cut the selected projects list based on available funding

## Slide 10: Weighted Score Method Top Ranked Projects
Rank | ID# | Project Name | Sponsor | Eligible Funding
1 | 21 | Black Forest Road Improvements | El Paso County | Safety, STP-Metro, FASTER
2 | 27 | Briargate Pkwy/ Stapleton Rd Connection | El Paso County | PPRTA, STP-Metro, FASTER
3 | 142 | Squirrel Creek Road Extension (Phases 2 and 3) | Fountain | STP-Metro
4 | 110 | Powers Blvd. (SH 21) Widening | Colorado Springs and CDOT | STP-Metro
5 | 72 | I-25 HOV Lanes | CDOT | 7th Pot/FASTER
6 | 123 | Route 6 Phase 4 Enhancements | Colorado Springs | TAP
7 | 10 | Academy Blvd. | El Paso County | Bridge-On, Bridge-Off, STP-Metro, Safety, FASTER
8 | 116 | Route 1 and 7 Phase 2 Enhancements | Colorado Springs | TAP
9 | 120 | Route 16 Phase 2 Enhancements | Colorado Springs | TAP
10 | 117 | Route 12 Phase 4 Enhancements | Colorado Springs | TAP
11 | 121 | Route 6 Phase 2 Enhancements | Colorado Springs | TAP
12 | 105 | Powers Blvd. (SH 21) Freeway | CDOT | 
13 | 91 | Mesa Ridge Parkway Extension: Powers Blvd to Marksheffel Road | El Paso County and Fountain | STP-Metro/PPRTA
14 | 62 | Garrett Road | El Paso County | Safety, STP-Metro, FASTER
15 | 6 | 8th Street Corridor Improvement Project | Colorado Springs | STP-Metro

## Slide 11
03
Technique of Order Preference by Similarity to Ideal Solution (TOPSIS)

## Slide 12: TOPSIS Method
Supports evaluation of three criteria types:
    Qualitative benefits
    Quantitative benefits
    Cost attributes or criteria
Can be used to evaluate benefits (more is better), costs (less is better) or both
Ranks projects based geometric distance (proximity) to the ideal project and (separation) from the negative ideal project, where:
  The ideal alternative/project has the best score for all criteria
  The negative ideal alternative/project has the worst score for all criteria

## Slide 13: TOPSIS Ranking Process
Construct normalized score decision matrix
Construct weighted, normalized score decision matrix
Determine ideal and negative ideal projects
Calculate separation measures (from ideal and negative ideal) for each project
Calculate measures of relative closeness to ideal for each project
Rank projects by order of closeness to the ideal project
Cut projects from the selected projects list based on available funding

## Slide 14: TOPSIS Top Ranked Projects
Rank | ID# | Project Name | Sponsor | Eligible Funding
1 | 72 | I-25 HOV Lanes | CDOT | 7th Pot/FASTER
2 | 27 | Briargate Parkway/ Stapleton Road Connection | El Paso County | PPRTA, STP-Metro, FASTER
3 | 142 | Squirrel Creek Road Extension (Phases 2 and 3) | Fountain | STP-Metro
4 | 136 | SH 85 Widening | CDOT | 
5 | 210 | US 24 West/Ridge Road Overpass | CDOT | 
6 | 40 | Dublin Road Widening: Peterson Road to Marksheffel Road | Colorado Springs | STP-Metro
7 | 91 | Mesa Ridge Parkway Extension: Powers Blvd to Marksheffel Rd. | El Paso County and Fountain | STP-Metro/PPRTA
8 | 62 | Garrett Road | El Paso County | Safety, STP-Metro, FASTER
9 | 110 | Powers Boulevard (SH 21) Widening | Colorado Springs and CDOT | STP-Metro
10 | 74 | I-25 Widening | CDOT | 7th Pot/FASTER
11 | 115 | Powers Boulevard: SH 83 to I-25 (at Northgate Rd) | Local, Private, CDOT | Local, Private, FASTER
12 | 111 | Powers Boulevard (SH 21) Widening | CDOT | 
13 | 205 | US 24 East Widening | CDOT | 
14 | 113 | Powers Boulevard (SH 21)/Stewart Interchange | CDOT | 
15 | 71 | Highway 105 | El Paso County | Safety, STP-Metro, FASTER

## Slide 15
04
Logic Scoring of Preference (LSP)

## Slide 16: LSP Method
Mimics human brain’s decision making process
Uses full continuum of logic functions OR (Yes/No) through AND to capture interdependencies among criteria and projects
Requires construction of a decision model upfront – preference aggregation structure
The model results are as good as the decision model – construction requires a collaborative process such as that used to develop evaluation criteria weighting

## Slide 17: LSP Logic Function Continuum
Name | Symbol | c, 1-q | d,q | r2 | r3 | r4 | r5
DISJUNCTION (OR) | D | 0.0000 | 1.0000 | + ∞ | + ∞ | + ∞ | + ∞
STRONG QD (+) | D++ | 0.0625 | 0.9375 | 20.63 | 24.30 | 27.11 | 30.09
STRONG QD (-) | D+- | 0.1250 | 0.8125 | 5.802 | 6.675 | 7.316 | 7.819
MEDIUM QD | DA | 0.2500 | 0.7500 | 3.929 | 4.450 | 4.825 | 5.111
WEAK QD | D- | 0.3750 | 0.6250 | 2.018 | 2.187 | 2.302 | 2.384
SQUARE MEAN | SQU | 0.3768 | 0.6232 | 2.000 |  |  | 
ARITHMETIC MEAN | A | 0.5000 | 0.5000 | 1.000 | 1.000 | 1.000 | 1.000
WEAK QC | C-- | 0.5625 | 0.4375 | 0.619 | 0.573 | 0.548 | 0.526
GEOMETRIC MEAN | GEO | 0.6667 | 0.3333 | 0.000 |  |  | 
WEAK QC (+) | C-+ | 0.6875 | 0.3125 | -0.148 | -0.208 | -0.235 | -0.251
HARMONIC MEAN | HAR | 0.7726 | 0.2274 | -1.000 |  |  | 
STRONG QC (-) | C+- | 0.8750 | 0.1250 | -3.510 | -3.114 | -2.823 | -2.606
STRONG QC (+) | C++ | 0.9375 | 0.0625 | -9.060 | -7.639 | -6.689 | -6.013
CONJUNCTION (AND) | C | 1.0000 | 0.0000 | -∞ | -∞ | -∞ | -∞

## Slide 18: LSP Logic Function Example - Advantages
Simple Binary logic - YES = 1 or 100%; NO = 0 or 0%
Or, in a simple weighted average of 3 projects:
Total Preference = w1 *S1 + w2*S2 + w3*S3
The scores (S’s) and the weights (w’s) have no logic – w choices are ad hoc and the preference for one project or another can be just YES or NO (1 or 0 ), no matter what is the score.
Results can be severely biased and do not link AND and OR preferences, or if it does, the choices are only YES or NO.
So, if you want to “AND” (or add a EXTREMELY NECESSARY criterion for choosing), or if you want to append a useful but not extremely necessary criterion say A “OR” B, both of these functions lack the “MAYBE” character. A preference could be 65% A “AND” B and 35% A “OR” B.
Scoring with this technique allows preferences to be spread over many projects and
the combination of ANDs and ORs are not just YES and NOs , but X% YES, and Y% NO.

## Slide 19
Formal Logic Tables (YES=1, NO =0)
ONLY YES ( APPEND) IF ALL CHOICES ARE 100% IN FAVOR
IF ANY CHOICE IS YES, THAT CHOICE CONTROLS THE RESULT.
LIFE IS JUST NOT THIS WAY: I MAY WANT “A” AND “B” TOGETHER WITH A 60% WISH VALUE BUT ALSO “D” OR “C” WITH A 67% WISH VALUE. LSP DOES JUST THAT – NO HARD “A” AND “B”, OR HARD “C” OR “D”, BUT A SPECTRUM OF PREFERENCES
A | B | A “AND” B
0 | 0 | 0
1 | 0 | 0
0 | 1 | 0
1 | 1 | 1
C | D | C “OR” D
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 20: LSP Ranking Process
Construct decision model – preference aggregation structure
Construct normalized score decision matrix
Construct weighted, normalized score decision matrix
Compute the elementary preference scores for each project
Compute aggregated preference score including all elementary preference scores
Rank projects by order of aggregated score
Cut the selected projects list based on available funding

## Slide 21: LSP Top Ranked Projects
Rank | ID# | Project Name | Sponsor | Eligible Funding
1 | 72 | I-25 HOV Lanes | CDOT | 7th Pot/FASTER
2 | 71 | Highway 105 | El Paso County | Safety, STP-Metro, FASTER
3 | 64 | Grinnell Boulevard | El Paso County | Safety, STP-Metro, FASTER
4 | 60 | Fountain over Spring Creek Rehabilitation | Colorado Springs | Bridge-Off
5 | 69 | Historic Bridges Repair and Restoration | Manitou Springs | Bridge-Off
6 | 110 | Powers Boulevard (SH 21) Widening | Colorado Springs and CDOT | STP-Metro
7 | 66 | Hancock Eastbound over Spring Creek Bridge Rehabilitation | Colorado Springs | Bridge-Off
8 | 79 | Jones Road | El Paso County | Safety, STP-Metro, FASTER
9 | 75 | I-25/Powers Blvd. (SH 21) North Interchange | CDOT | 
10 | 105 | Powers Blvd. (SH 21) Freeway | CDOT | 
11 | 62 | Garrett Road | El Paso County | Safety, STP-Metro, FASTER
12 | 109 | Powers Boulevard (SH 21) Water Quality Improvements | CDOT | 
13 | 108 | Powers Boulevard (SH 21) Safety Improvements | CDOT | 
14 | 107 | Powers Boulevard (SH 21) Right-of-Way | CDOT | 
15 | 68 | Hancock Phase Westbound over Spring Creek Bridge Rehabilitation | Colorado Springs | Bridge-Off

## Slide 22
05
How should we rank and select projects for the fiscally constrained Regional Transportation Plan?

## Slide 23: Model 1 – Weighted Score Method Easily understood and easy to apply Requires consistent criteria (benefits or costs) Does not capture interdependencies among criteria and projects Model 2 – TOPSIS Method Less easily understood but easy to apply Allows evaluation of multiple criteria types Does not capture interdependencies among criteria and projects Model 3 – LSP Method Model specification is relatively complex Allows evaluation of multiple criteria types Can capture interdependencies among criteria and projects Often has more than 1 “Optimal Solution”
MCDM Method Comparison

## Slide 24: Questions?