## Slide 1: Forecasting Weekend Travel Demand Using an Activity-Based Model System
Bhargava Sana, SFCTA
TRB Planning Applications Conference
May 17, 2017 Raleigh, NC

## Slide 2: Acknowledgements
  Rosella Picado, WSP
  Raghu Sidharthan, WSP
  Dora Wu, WSP
  Priyoti Ahmed, SFCTA
  Joe Castiglione, SFCTA
Notes: I would like to first acknowledge the contributions of our consultant team and my colleagues at SFCTA, including…

## Slide 3: Treasure Island Context
  20,000 residents by 2035
  retail, office/commercial, and public space uses.
  Access only the San Francisco-Oakland Bay Bridge
    Tolling on and off island
  Operation and financial solution requires consideration of weekend
    Traffic impact analyses
    Revenue forecasts
Treasure Island
Notes: Treasure Island is an island located in the middle of the San Francisco Bay. For those of you have been the to the Bay Area it is the midpoint between the eastern and western spans of the San Francisco Bay Bridge. Originally built for an international exhibition, it later became a military base. When the base was closed, redevelopment plans for the island were approved, which will result in over 20,000 residents living on the island by 2035. A critical issue is access on/off the island, as the only existing connection is via the Bay Bridge, which is already saturated with demand throughout most of the day. In order to mange this demand, the SFCTA was identified as the mobility management agency for the island. In this role, the SFCTA will be setting and collecting tolls to access the island, and using these funds for providing alternatives such as new ferry service and increased bus service.

## Slide 4: Forecasting Challenge
  SF-CHAMP
    ABM
    Entire Bay Area
    Typical weekday
  Challenges
    Limited observed data on weekend travel
    No weekend models estimated
    Schedule
Notes: The SFCTA needed to generate traffic and revenue forecasts to support planning of Treasure Island transportation options. The SFCTA’s primary tool for forecasting travel demand is our SF-CHAMP activity-based travel demand forecast model. This model covers the entire bay area, and includes a rich representation of the regional transportation system including sensitivities to tolls. However, like most travel models, it is a “typical weekday” model. This is a significant limitation, as Treasure Island includes extensive recreation and special event facilities, and many of these types of activities are anticipated to occur on weekend. The limited amount of weekend data, absence of weekend models, and a constrained project schedule represented significant challenges to developing reasonable weekend travel demand and revenue forecasts..

## Slide 5: Solution
  Tour resampling
    Weekday activities (tours) to match weekend travel patterns
  Run subsequent choice models
    Mode
    Destination
    Trip models
  Recalibrate to weekend targets
  Integrate special event demand
Work Location
Vehicle Availability
Weekday Tour Gen
Weekend Resampling
Tour Destination
Tour Mode
Stop Location
Trip Mode
Network Assignment
Network Skim
3 global iterations
4 simulations / iteration
Notes: In response to these constraints, the modeling team developed and implemented a “tour resampling” approach to generating estimates of weekend demand. Rather than attempt to estimate weekend models with limited data and a tight schedule, instead the team implemented an approach in which weekday tours are resampled to match weekend tour targets, segmented by purpose, person type, and broad time period combination. Once this set of weekend tours has been generated, all of the subsequent choice models in SF-CHAMP are executed, including tour destination and mode, and trip stop location and mode. The model system is run in a manner consistent with the execution of the weekday models, which includes running three global iterations, and four full simulations within each global iteration, to attenuate simulation variation.

## Slide 6: Tour Resampling
  Tour targets set by person type, purpose, time period combination
  For each tour type, target is specified as either
    Fractional share
    Absolute number (easier)
  Based on weekday tourgen results, scale factors calculated
  Tours randomly sampled without replacement until target is reached
 | Worker | Student | Other | Child | Total
Work | 674,465 | 36,254 | 48,398 |  | 759,125
Gradeschool |  |  |  | 57,236 | 57,236
Highschool |  | 8,297 |  | 8,620 | 16,917
College | 12,012 | 11,574 | 8,239 |  | 31,825
Other | 3,830,715 | 567,356 | 1,858,815 | 1,090,011 | 7,346,898
Work-based | 113,681 |  |  |  | 113,689
Total | 4,630,873 | 623,482 | 1,915,461 | 1,155,876 | 8,325,691
Tour Targets
Chart: Tour Time of Day
| Early | AM peak | Midday | PM peak | Evening
Weekday | 0.028366 | 0.36611 | 0.38345 | 0.13764 | 0.084427
Weekend | 0.014867 | 0.18614 | 0.56675 | 0.17067 | 0.061567
Notes: Resampling tour targets were segmented by person type, purpose, and time period combination. This made it possible to match the observed weekend travel markets reasonably well, These tour targets can be set as either fraction shares or as absolute targets. For the TIMMA project, we used absolute targets, which facilitated easy adjustment to better match observed network volumes. Once the targets are established, tours are randomly sampled without replacement until the target is reached. The charts on the right hand side of this slide illustrate some of the differences between weekday and weekend travel patterns on, with more shared ride tours on weekends, and tours generally happening later in the day. You can also see that there are relatively few work or school tours on the weekend, but a huge number of “other” tours.

## Slide 7: Benefits
  Implement quickly
  Avoid re-estimating weekend demand models
  Avoid application code rewrite
  Incorporate most of ABM sensitivities
  Provides full range of disaggregate ABM outputs
    Assessment of the equity impacts of tolling on both existing as well as new island residents.
Work Tours
Other Tours
Weekday
Weekend (sampled)
Notes: There are a number of benefits to this approach. First, it allowed us to get a weekend model up and running relatively quickly because it avoided the need to re-estimate weekend demand models which would have been challenging given the limited weekend data. This approach also avoided the need for any core application code adjustments, although additional scripting was required to implement the re-sampling, and to integrate the resampled weekend demand with the overall model runstream. A second benefit of the approach was that it incorporated most of the sensitivities to mode, destination, and time-of-day that are incorporated in the weekday model. Finally, it provided the full set of disaggregate model outputs. This was very important, as one of the key policy issues in redeveloping the island is accounting for and understanding the impacts on the current existing residents, many of whom will continue to live on the island after redevelopment.

## Slide 8: Calibration / Validation
  Tour resampling
  Tour destination
  Tour mode
  Tour time of day
 | Survey | Model
Drive Alone | 26.1% | 26.6%
Shared Ride 2 | 25.7% | 23.5%
Shared Ride 3+ | 30.5% | 31.3%
Walk | 11.8% | 12.6%
Bike | 2.2% | 2.4%
Walk-Local Bus | 1.7% | 1.4%
Walk-LRT | 0.5% | 0.6%
Walk-Premium Bus | 0.1% | 0.0%
Walk-Ferry | 0.0% | 0.0%
Walk-BART | 0.5% | 0.5%
Drive-Local Bus | 0.0% | 0.0%
Drive-LRT | 0.0% | 0.0%
Drive-Premium Bus | 0.0% | 0.0%
Drive-Ferry | 0.0% | 0.0%
Drive-BART | 0.6% | 0.5%
Taxi | 0.2% | 0.4%
Total | 100.0% | 100.0%
Depart | Return | Survey | Model
Early | Early | 0.2% | 0.2%
 | AM peak | 0.2% | 0.2%
 | Midday | 0.9% | 0.8%
 | PM peak | 0.1% | 0.1%
 | Late | 0.1% | 0.1%
AM peak | AM peak | 2.2% | 2.4%
 | Midday | 11.6% | 11.5%
 | PM peak | 2.5% | 2.1%
 | Late | 2.2% | 1.9%
Midday | Midday | 35.9% | 37.3%
 | PM peak | 14.0% | 13.9%
 | Late | 6.7% | 6.1%
PM peak | PM peak | 7.7% | 7.6%
 | Late | 9.3% | 9.3%
Late | Late | 6.2% | 6.6%
Total | Total | 100.0% | 100.0%
Notes: As often occurs with weekday model implementation, it was necessary to adjust the weekend tour targets to better match observed network volumes. Some additional calibration of the tour and trip mode and destination models was also performed. This recalibration effort did require some additional time, but was completed in approximately one month. The result was a model system that matched weekend-based targets for invidual model components as well network assignments relatively well. The tables on the right illustrate the observed to estimated shares for the tour time period combinations and trip modes.

## Slide 9: Results & Conclusions
  Results
    Higher trip-making on weekend than weekday
    Non-resident weekend trips lower in 2020 due to no special events
  Resampling Conclusions
    Cost-effective
    Met schedule
    Provided almost all model sensitivity and reporting capabilities
    Reasonable results
Chart: Trips by Day and TI Residency Status
| Weekday TI Residents | Weekend TI Residents | Weekday Non-TI Residents | Weekend Non TI-Residents
2015 | 6248 | 7742 | 4466 | 8639.2237
2020 | 9833 | 12576 | 4560 | 5077.6851
2025 | 23773 | 30704 | 6485 | 11699.9615
Notes: The results showed high levels of trip-making by both residents and non-residents on the weekend. Although it should be noted that some of the non-resident demand is due to special events. In conclusion the tour resampling approach proved to be cost-effective, met our schedule provided almost all the capabilities of the weekday model, and produced reasonable results.

## Slide 10: contact: bhargava.sana@sfcta.org